## Slide 1: Fusion of Indirect Methods and Iterative Learning for Persistent Velocity Trajectory Optimization of a Sustainably Powered Autonomous Surface Vessel
Kavin M. Govindarajan, Devansh R Agrawal, Dimitra Panagou, Chris Vermillion
CCTA 2025

## Slide 2: Outline
Motivation
Problem Formulation
Methodology
Real-Time Realization & Results
Conclusion & Future Work

## Slide 3: Why do we want to run persistent missions?
Two features:
Data varies with space and time
We want to collect data over long periods of time
[1] K. Haas, “Assessment of energy production potential from ocean currents along the United States coastline,” Georgia Inst. of Technology, Atlanta, GA (United States), Tech. Rep., 2013.
[2] Bane, John, et al. "Atmospheric forcing of the Hatteras coastal ocean during 2017–2018: The PEACH program." Dynamics of Atmospheres and Oceans 102 (2023): 101364.
160 TWh/yr of Technical Energy Capacity ~ 14.5 million homes [1]
Marine Hydrokinetic Energy -
Flow Velocity vs Depth Data
Understanding Ocean Circulation -
Sea Surface Salinity (SSS)
Mean SSS off the Atlantic Coast of the United States [2]

## Slide 4: A Solar-powered ASV
SeaTrac SP-48 ASV
Attribute | Value
Length | 4.8 meters
Beam | 1.39 meters
Draft | 0.42 meters
Weight | 300 kilograms
Solar Panel Area | 4.17 meters2
Brushless Motor | 500 Watts
Battery Capacity | 6.75 kiloWatt Hours
Top Speed | 4.5 knots
Cruise Speed | 3 knots

## Slide 5: How can we control the ASV?
Direction:
Speed:
Finite horizon
Infinite horizon
  “Segmented” missions via recharging [3][4]
  Finite-horizon MPC with terminal reward for infinite-horizon performance [5]
[3] B. Haydon, J. Reed, and C. Vermillion, “Persistent mission planningof an energy-harvesting autonomous underwater vehicle for gulf streamcharacterization,” IEEE Transactions on Control Systems Technology,vol. 32, no. 2, pp. 653–662, 2023.
[4] G. Notomista, C. Pacchierotti, and P. R. Giordano, “Online robottrajectory optimization for persistent environmental monitoring,” IEEEControl Systems Letters, vol. 6, pp. 1472–1477, 2021.
[5] K. Govindarajan, B. Haydon, and C. Vermillion, “Predictive velocitytrajectory control for a persistently operating solar-powered autonomoussurface vessel,” in 2023 American Control Conference (ACC), 2023, pp.2077–2083.

## Slide 6: What are we trying to solve?
We seek to maximize distance as a proxy for information!
Battery dynamics
Battery constraint
Speed constraint
To solve this:
NLOpt solver-> difficult to converge to a solution
Indirect methods -> messy singular arcs

## Slide 7: Why is this difficult to solve?

## Slide 8: Why is this difficult to solve?

## Slide 9: Why is this difficult to solve?

## Slide 10: Lower SOC Constraint

## Slide 11: Upper SOC Constraint

## Slide 12: Why is this difficult to solve?

## Slide 13: What are we trying to solve?
We can now solve this using indirect methods!!

## Slide 14: The Control Solution

## Slide 15: How do we solve for the costate?
is piecewise constant!!

## Slide 16: Model Predictive Control

## Slide 17: How do we solve for the costate?
is piecewise constant!!

## Slide 18: Iterative Learning Update Law

## Slide 19: How do we solve for the costate?
is piecewise constant!!

## Slide 20: Comparison Constant Velocity Strategies
2 Cases:
Constant velocity w/ SOC constraints
Constant velocity w/o SOC constraints

## Slide 21: Real time realization: Irradiance models
Ideal Irradiance Model [6]
Historical Irradiance Model: ERA5 [7]
[6] R. L. Hulstrom, Insolation Models and Algorithms, 2003, pp. 61–141.
[7] H. Hersbach, B. Bell, P. Berrisford, S. Hirahara, A. Horányi, J. Muñoz-Sabater, J. Nicolas, C. Peubey, R. Radu, D. Schepers, et al., "The ERA5 global reanalysis," Quarterly Journal of the Royal Meteorological Society, vol. 146, no. 730, pp. 1999–2049, 2020.

## Slide 22: Real time realization: Results
Ideal Irradiance Model
Historical Irradiance Model

## Slide 23: Conclusion
Takeaways:
Proposed ILC approach nearly matches MPC performance w/o need for a forecast
Proposed ILC approach is less computationally intensive
  MPC: 21 hrs 36 min
  ILC: 20 seconds
Ongoing work:
Real-world information-gathering mission
Swapping distance metric for information metric
Supported by: NSF Award Number 2223844
Questions?
Email: kmgovind@umich.edu
Github: https://github.com/kmgovind/persistent-speed-control

## Slide 24: Backup Slides

## Slide 25: Questions?
Supported by: NSF Award Number 2223844

## Slide 26: How do we collect oceanographic measurements?

## Slide 27: Revised Constraints

## Slide 28: Iterative Learning Update Law
Daily Update (Proportional Learning Gain):
where is the proportional learning gain and is the desired terminal state of charge at the end of the iteration.
At each timestep in iteration (Continuous Rate-Based Gain):
where is a rate-based gain.

## Slide 29: Characterizing as a mathematical function [3]
[3] R. L. Hulstrom, Insolation Models and Algorithms, 2003, pp. 61–141.

## Slide 30: in the real world: ERA5 Model [4]
[4] Hersbach, Hans, et al. "The ERA5 global reanalysis." Quarterly journal of the royal meteorological society 146.730 (2020): 1999-2049.

## Slide 31: Results – Model Irradiance

## Slide 32: Results – Real World Irradiance

## Slide 33: Applying Indirect Methods
Hamiltonian:
State Equations:
Costate/Adjoint Equations: